## Slide 1: Automation Starter Kit: Skid Assembly Details
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Main Components
Saddle Assembly
  Saddle plate
  Support plate
  Bottom Plate
Skid Beams
Skid Assembly

## Slide 3: Saddle Assembly
Weldment assembly with three components
Main Driving Parameters:
  TANK_OD
  SKID_FW
  SKID_FH
  SKID_FL_THK
  SKID_WEB_THK
  SKID_FLG_RAD
  SKID_W
  SAD_TOP_THK
  SAD_W
  SAD_OFF

## Slide 4: Saddle Assembly
Component Rules:
  Update Parameters
    Just pushes important parameters down to the individual components so all parts are sized properly

## Slide 5: Saddle Assembly
Important Modeling Note:
  All three parts in the skid assembly were created in context of how they would appear inside the assembly
  This means that if we assemble each component at the origin of the assembly, all parts are properly sized and in the right place
  This makes it easy to drive changes in the model

## Slide 6: Saddle Assembly – Saddle Plate
Sheet Metal component (named Skid-1.ipt)
Main Driving Parameters:
  TANK_OD
  SKID_FW
  SKID_FH
  SAD_TOP_THK
  SAD_W

## Slide 7: Saddle Assembly – Saddle Plate
Component Rules:
  Set Sheet Metal Style
    Sets the part to the correct sheet metal style, based on desired thickness

## Slide 8: Saddle Assembly – Support Plate
Sheet Metal component (named Skid-2.ipt)
Has two variations:
  One is for when the skid uses I-beams
  The other is for when the skid uses rectangular beams
Main Driving Parameters:
  TANK_OD
  SKID_FW
  SKID_FH
  SKID_FL_THK
  SKID_WEB_THK
  SKID_FL_RAD
  SAD_OFF
  SAD_TOP_THK
  SAD_W

## Slide 9: Saddle Assembly – Saddle Plate
Component Rules:
  Set Sheet Metal Style
    Sets the part to the correct sheet metal style, based on desired thickness

## Slide 10: Saddle Assembly – Bottom Plate
Sheet Metal component (named Skid-3.ipt)
Main Driving Parameters:
  TANK_OD
  SKID_FW
  SKID_FH
  SKID_FL_THK
  SAD_W
Component Rules:
  None

## Slide 11: Skid Beams
Beams supports for the skid assembly
I-Beams used for tank OD 36” and above
Rectangular beams used for OD 24” and 30”
Main Driving Parameters:
  TANK_OD
  TANK_L
  SKID_FW
  SKID_FH
  SKID_FL_THK
  SKID_WEB_THK
Component Rules:
  None
  SKID_WEB_THK
  SKID_F_OFFSET
  SKID_R_OFFSET
  SKID_BEND_L
  SKID_ROD_D

## Slide 12: Skid Assembly
  SAD_BTM_THK
  SAD_TOP_THK
  SAD_W
  SAD_OFF
  SHELL_W_1
  SHELL_Q_1
Main assembly for skid
Main Driving Parameters:
  PROJECT_ID
  PROJECT_PATH
  TEMPLATE_PATH
  TANK_OD
  TANK_L
  SKID_FW
  SKID_FH
  SKID_FL_THK
  SKID_WEB_THK
  SKID_FL_RAD
  SKID_W
  SHELL_W_2
  SHELL_Q_2
  SKID_BEND_L
  SKID_ROD_D
  DISH_DEPTH

## Slide 13: Skid Assembly
Component Rules:
  Create Skid
    Checks if OD is 30” or less
      Replaces I-beam, if that is true
    Creates a copy of the saddle assembly
    Renames component occurrences in assy
    Adds saddle assemblies between the beams, and places each one individually
      Uses constraints to put these together
  Has a “CopyComponents” subroutine
    Is a basic “copy design” rule that copies all parts in an assembly to a new location, and then sets the assembly to reference the new files

## Slide 14: Skid Assembly
Component Rules:
  Update Saddle Parameters
    Pushes driving parameters from skid assembly into the skids and saddle assembly, as required