## Slide 1: Automation Starter Kit: Overview of Dataset
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Main Components
Tank Body
Skid Assembly
Gunline Assembly
Manways and Hatches
Inlets and Drains
Sumps
End Connections

## Slide 3: Tank Body
Made up of two primary components:
  Dish head
  Individual shell pieces
Valid Diameters:
  24” – 144”: 6” increments
Valid Lengths:
  36” – 600”: 6” increments

## Slide 4: Skid Assembly
Made up of two components:
  Skid Beams
  Saddle Assemblies
Lengths and Widths:
  Based on tank body dimensions

## Slide 5: Gunline Assembly
Made up of three components:
  Feed line
  Spray nozzles
  End connections
Lengths and Widths:
  # of spray nozzles is the same as the # of shell plates required for the shell body
  Two size options:
    4” or 6”

## Slide 6: Manways and Hatches
Manway and Hatch Models:
  Model for each variation is static
Manway Sizes:
  21”, 22” or 25”
  Only for tanks with OD 48” or higher
  Always on rear side of tank
Hatch Size:
  20” (just one option)
  Only for tanks with OD 60” or higher
  Always on top side of tank
  Optional front and rear placements

## Slide 7: Inlets and Drains
Inlets Made up of two components:
  Tube
  End connection
Inlet Sizes:
  3”, 4”, 6” or 8”
Locations on Tanks:
  Inlets can be on top or front of tank
  Drains are at the bottom
    Can choose to have drains on front, rear or both

## Slide 8: Sumps
Made up of four components:
  Sump bracket
  Angle pipe
  Straight pipe
  End connection
Configurable Options:
  Two sizes: 6” or 8”
  Height for sump outlet
  Projection length from tank for the outlet
  End connection type

## Slide 9: Flange Options
Flanges:
  Sizes: 3”, 4”, 6” or 8”
  Lapped
  Slip-On Welding
  Welding Neck
End Connections:
  Open (just the flange)
  Capped (with blind flange)
  Valve (butterfly w/threaded flange)