## Slide 1: Automation Starter Kit: Gunline Assembly Details
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Main Components
Gunline Feed Pipe
Gunline Down Pipe
Elbow – 45-degrees
Reducer
End Connections
Gunline Assembly

## Slide 3: Gunline Feed Pipe
Pipe that feeds the gunline system
Main Driving Parameters:
  G_H (OD of gunline)
  G_T (pipe thickness)
  G_OFFSET_START
  G_OFFSET_END
  GUNLINE_L
  NO_NOZZLES
  NOZZLE_SPACING
  NOZZLE_1_OFF
Component Rules:
  None

## Slide 4: Gunline Down Pipe
Library of static parts
Rule in gunline assembly will select the proper length and size (diameter), and insert it into the assembly
Main Driving Parameters:
  Diam (OD of pipe
  ParT (thickness of pipe)
  B_L (length of pipe)
  G_OFFSET_START
  G_OFFSET_END
Component Rules:
  None

## Slide 5: Elbow – 45 Degrees
Library of static parts
Two parts for application to choose from:
  2” part (for 4” gunline)
  4” part (for 6” gunline)
Main Driving Parameters:
  OD (OD of pipe)
  T (pipe thickness)
Component Rules:
  None

## Slide 6: Reducer
Library of static parts
Two parts for application to choose from:
  2” part (for 4” gunline)
  4” part (for 6” gunline)
Main Driving Parameters:
  OD1 (OD of pipe)
  OD2 (Reduced OD)
  T1 (pipe thickness)
  T2 (reduced pipe thickness)
Component Rules:
  None

## Slide 7: End Connections
Have options to choose from the following sizes:
  3”, 4”, 6” or 8”
  Flanges:
    Lapped
    Slip-On Welding
    Welding Neck
  End Connections:
    Open (flange only)
    Capped (with blind flange)
    Valve (butterfly)
Each end of gunline may have a different end connection selected

## Slide 8: Gunline Assembly
  SHELL_Q_1
  SHELL_Q_2
  GUNLINE_OFF
  GUNLINE_SIZE
Main assembly for gunline
Main Driving Parameters:
  PROJECT_ID
  PROJECT_PATH
  TEMPLATE_PATH
  LIBRARY_PATH
  TANK_OD
  TANK_L
  GUNLINE_L
  NO_NOZZLES
  NOZZLE_SPACING
  NOZZLE_1_OFF
  GUNLINE_F_FL_TYPE
  GUNLINE_F_FL_END
  GUNLINE_R_FL_TYPE
  GUNLINE_R_FL_END

## Slide 9: Gunline Assembly
Component Rules:
  Set Gunline Size
    Replaces 4” feed pipe with 6” pipe if user requests 6” pipe
      Assembly template has a 4” feed pipe pre-placed at assembly’s origin
    Creates a new feed pipe and saves it in the correct folder
    Replaces the feed pipe in the new gunline assembly file with the new copy just created
    Rebuilds a constraint that was breaking as I was creating the template

## Slide 10: Gunline Assembly
Component Rules:
  Calculate Gunline Spacing
    Simple rule that calculates the following, and sets them to the right parameter:
      Length of the gunline
      Number of required nozzles
      Spacing between nozzles
      Offset for where the first nozzle starts on the gunline pipe
  These parameters are then used to set the length of the feed pipe, and drive the pattern of the downpipe assemblies

## Slide 11: Gunline Assembly
Component Rules:
  Push Parameters
    Simple rule that pushes calculated values from the previous rule into the feed pipe so that it sizes itself appropriately

## Slide 12: Gunline Assembly
Component Rules:
  Spray Nozzle Length
    Rule that finds the appropriate down pipe, and replaces it in the assembly
    Uses a Select Case statement in Visual Basic, and is a good example of how these work

## Slide 13: Gunline Assembly
Component Rules:
  Assemble Flanges
    Most complex rule in this assembly
    Gets the right offset value depending on if a flange or valve has been selected
    Defines assembly placement matrix of front and rear flanges / valves
    Based on options selected, decides which library model to pull into the assy
      Does this for both front and rear
    Adds the components into the assembly
  Has a function called “FindOffsetValue” that figures out how far the flanges or valves should be offset so they are placed properly