## Slide 1: Automation Starter Kit: Manway & Hatch Details
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Main Components
Manway
  21” Size
  22” Size
  25” Size
Hatch
  20” Size

## Slide 3: Manway – 21” Size
21” Manway assembly
Always located at rear of assembly
Only applicable to tanks with OD >= 48”
Static assembly located in the library
Top-level tank assembly will insert it based on matrix positioning
  Matrix positioning uses the point of origin to locate and orient the assembly
Component Rules:
  None

## Slide 4: Manway – 22” Size
22” Manway assembly
Always located at rear of assembly
Only applicable to tanks with OD >= 48”
Static assembly located in the library
Top-level tank assembly will insert it based on matrix positioning
  Matrix positioning uses the point of origin to locate and orient the assembly
Component Rules:
  None

## Slide 5: Manway – 25” Size
25” Manway assembly
Always located at rear of assembly
Only applicable to tanks with OD >= 48”
Static assembly located in the library
Top-level tank assembly will insert it based on matrix positioning
  Matrix positioning uses the point of origin to locate and orient the assembly
Component Rules:
  None

## Slide 6: Manway – Horizontal Placement
Each manway has a slightly different origin point in the Z-axis of the tank
Several lines of code are used to set different Z-axis offsets, based on the specific manway inserted into the assembly
In general, it’s good practice to keep models of library components as consistent as possible so it doesn’t require a lot of extra code to handle different requirements

## Slide 7: Hatch – 20” Size
20” Hatch assembly – only one available
Always on top of tank body
Option to have them at front or at back of assembly
Only applicable to tanks with OD >= 60”
Static assembly located in the library
Top-level tank assembly will insert it based on matrix positioning
  Matrix positioning uses the point of origin to locate and orient the assembly
Component Rules:
  None