## Slide 1: Automation Starter Kit: Introduction to the Kit
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Agenda
What is the Starter Kit?
What’s in the Starter Kit
How to Get Started
Important Concepts
Demonstration and Overview

## Slide 3: What is the Starter Kit?
Purpose:
  To give a practical example of how to architect and automate a design process
Contents:
  Sample dataset that includes all necessary files and code to create an automated 3d model
  Documentation that helps familiarize users with contents and setup of the solution
Target Audience:
  Users that are new to design automation
Beneficial Pre-Requisites:
  Beginner Visual Basic programming knowledge

## Slide 4: What is the Starter Kit?
What is not included:
  Visual Basic tutorials or instruction
  Drawing automation functionality
  External rules for iLogic
  Building add-ins or plug-ins
  Using Visual Studio for solutions
  Debugging techniques or guidance
Inventor Software Requirements:
  Autodesk Inventor 2020 or higher

## Slide 5: What’s in the Starter Kit?
Main Parts of the Tank:
  Overall Tank Assembly
    Creating iLogic forms
    Reading data from Excel files
    Managing overall assembly creation
  Tank Body Assembly
    Using iParts in solutions
    Creating assemblies with constraints
    Suppressing assembly-level features
  Skid Assembly
    Subbing out parts in sub-assemblies
    Pushing parameters to sub-assemblies
  Gunline Assembly
    Using Select…Case commands
    Subbing library components in assemblies

## Slide 6: What’s in the Starter Kit?
Main Parts of the Tank:
  Manway Assembly
    Tank selects and inserts proper manway based on several possible sizes
  Hatch Assembly
    Inserted in front, back or both
  Inlet
    Inserted on top or front of tank
  Drains
    Inserted in front, back or both
  Sump
    Trig used to calculate angled pipe length
    Uses Try…Catch Visual Basic functionality
    Combines library and project-specific parts

## Slide 7: How to Get Started
Step 1: Download the Kit (provide link here?)
Put a screenshot of the web page here (along with the address)

## Slide 8: How to Get Started
Step 2: Unzip all files
Recommended deployment:
  Create a new folder on the C:\
  Name it “Automation Starter Kit”
    All capitalization and spacing needs to be exact
  Unzip files in this new folder
    Make sure the unzip tool does not create a new folder
  Folder structure should look similar to the screenshot shown to the right once all files and folders are unzipped

## Slide 9: How to Get Started
Step 3: Set the Project File
Open Inventor
  Click “Projects” command on the ribbon
  In the Project window, click “Browse…” button
  Navigate to where files were unzipped
  Select the “Automation Starter Kit” project file
  Click “Open”

## Slide 10: How to Get Started
Step 4: Open the Assembly
Open assembly to run the automation
  Make sure that the new “Automation Starter Kit” project is active
  Click “Open” in the Inventor interface
  Make sure you are in the “Workspace” directory
  Double-click the “Create New Tank.iam” file
  The file opens and displays the “Configure Tank” dialog box
    Note that there is no geometry in this file (it will be blank)
    Geometry will be created once you click the “Create New Tank” button

## Slide 11: How to Get Started
Step 5: Additional Setup (if required)
If the files are not unzipped in proper folder structure, follow these steps:
  With the “Create New Tank” assembly open, click on the Parameters command to open the interface
  Update the PROJECT_PATH, LIBRARY_PATH, and TEMPLATE_PATH parameters
    Note you MUST include a “\” at the end of the paths for the automation to function properly
Update these three parameters with the
corresponding paths on your computer

## Slide 12: How to Get Started
Step 5: Additional Setup (if required)
If the files are not unzipped in proper folder structure, follow these steps:
  Next edit the “Create New Tank” rule in the iLogic interface
  Scroll down to the function that gets the parameters from Excel
  In that rule, update the hard-coded path to the “SK Excel File.xlsx” in all three applicable locations
  Save the “Create New Tank.iam” file with these changes applied
Update these three hard-coded paths in
these locations

## Slide 13: Important Concepts
Typical new design workflow
Placing components in assemblies
Passing parameters between files
Building code in sub-assemblies

## Slide 14: Typical New Design Workflow
Step 1: Make a copy of an existing design
Find another design that is similar to the new design that needs to be created
Make a new copy of the top-level assembly, and put it in a new location

## Slide 15: Typical New Design Workflow
Step 2: Make copies of components
For components that will need to be changed in the new assembly, new copies need to be made
This will allow us to modify and make changes to these components without adversely affecting the original assembly we copied from

## Slide 16: Typical New Design Workflow
Step 3: Update References
For the new assembly, we need to update the references to the newly copied component files
This is like the “Component > Replace” command inside of Inventor

## Slide 17: Typical New Design Workflow
Why is this important?
Having proper file management is key to a good automation solution
In code, we are basically doing this same process when we need new copies of parts and assemblies
This is the methodology used extensively in the Starter Kit
  InventorAssembly.SaveAs
  System.IO.File.Copy

## Slide 18: Placing Components in Assemblies
Two methods we can use to place components in an Assembly via iLogic:
  Use constraints
  Use matrices or points

## Slide 19: Placing Components in Assemblies
Using Constraints
  Reference model geometry
  Mate, Flush & Insert
iLogic snippet for creating mates
Easier way to add mates with iLogic:
  Insert component into existing assembly
  Add desired constraints manually
  Open the iLogic editor
  Right-click the component in the Model tab
  Select “Capture Current State”
    Components.Constraints.Add
  Save the rule
  Delete the component out of the assembly

## Slide 20: Placing Components in Assemblies
Using Points and Matrices
  Both place the part coordinate system in relation to the assembly coordinate system
  When Points are used:
    Orientation of part is same as assembly
    Just need location for the insert
  When Matrices are used:
    Part needs to be rotated in relation to the assembly to be properly placed

## Slide 21: Placing Components in Assemblies
How do matrices work?
  Matrix has 4 rows and 4 columns
  The top 3 x 3 rows and columns represent a unit vector for each major axis
    First three numbers in the left column represent the X-axis unit vector
    First three number in the second column represent the Y-axis unit vector
    First three numbers in the third column represent the Z-axis unit vector
    First three numbers in the last column represent the part offset from the Assembly origin
    Last row isn’t really used, so always leave it 0, 0, 0, 1
X-Axis
Y-Axis
Z-Axis
Offset
(1, 0, 0)
(0, 1, 0)
(X, Y, Z)

## Slide 22: Placing Components in Assemblies
Example of Matrix
  For the hatch in the rear of the tank, we need to rotate the hatch 180-degrees around the Y-axis
  What axis on the hatch is in the same direction of the X-axis on the tank?
    The answer is –X (-1, 0, 0)
  What axis on the hatch is in the same direction of the Y-axis on the tank?
    The answer is +Y (0, 1, 0)
  What axis on the hatch is in the same direction of the Z-axis on the tank?
    The answer is –Z (0, 0, -1)

## Slide 23: Placing Components in Assemblies
Example of Matrix
  What about the offset values?
    Notice where the origin points are in relation to each other in both models
    To place the hatch in the right location:
      Move 10.625” in the -X direction
      Move length of radius (TANK_OD / 2) in +Y-direction, plus a 3” offset
      Move it to the edge of the tank body (TANK_L / 2) in the -Z direction, then move it forward by 21.5” (width of hatch), then forward by offset chosen by user

## Slide 24: Placing Components in Assemblies
Example of Matrix
  Now let’s put it all together
  Combining the orientation matrix with the offset matrix, we get the final placement matrix as follows (see code that follows to see how this was written):

## Slide 25: Passing Parameters Between Files
iLogic has built-in code snippet to pass parameters from parent assembly to children components
Uses the occurrence names (located in the model browser), and not the filenames (they can be different)
Best practice is to name all parameters the same to make it easy to follow the logic between assemblies and components
Code snippet to pass parameters from assembly to child part
Component Instance Name
Name of the parameter to set in the child component

## Slide 26: Common Process in Starter Kit
The methods previously reviewed follow the process over and over again throughout the starter kit code
  First, create a new copy of the files needed
  Then make sure the assembly references the new files
  Then place the component into the top-level assembly
  Finally, pass parameters so the model updates and gets sized appropriately

## Slide 27: Building Code in Sub-Assemblies
Rather than building all the code in the top assembly, build code in sub-assemblies so they can update themselves
This makes the code easier to troubleshoot when there are problems
It is also easier to start automating sub-assemblies, then once you have them working, move up to the next level (and so on)
Good examples of this:
  Tank body sub-assembly
  Gunline sub-assembly
These rules will update the gunline once the parameters have been passed to it

## Slide 28: Overview and Demonstration
User Interface:
  Project ID: This is a required field, and must be unique for each tank
  Tank OD: Valid range is from 24” to 144”, in 6” increments
  Tank Length: Valid range is from 36” to 600”, in 6” increments
  Inlet Information:
    Only 1 inlet per tank
    May be placed on top, or on the front dish head plate
    Select offset from front of tank, or top of tank to place the inlet nozzle
    Select flange type and end connection

## Slide 29: Overview and Demonstration
Drain Info Options:
  Optional to have one drain in the front, and one drain in the rear of the tank
  Drains are always located centered at the bottom of the tank
  For each drain selected to place, may select the flange type and end connection for each one separately

## Slide 30: Overview and Demonstration
Tank Access Options:
  Manway:
    Only valid for tanks with OD 48” or larger
    Option to include it (or not)
    Can select size between three options (21”, 22” & 25”)
    Placed on rear dish of tank
  Hatches:
    Only valid for tanks with OD 60” or larger
    Option to include it (or not)
    Only one size, and always placed on top of tank body
    May select offset from each end based on desired location

## Slide 31: Overview and Demonstration
Gunline Info Options:
  Option only valid for tanks with OD 60” or larger
    Option to include it (or not)
    Can select between two sizes (4” or 6”)
    May select flange options for front and rear of gunline independently
    Flange options include flange type and end connection

## Slide 32: Overview and Demonstration
Sump Info Options:
  Option only valid for tanks with OD 60” or larger
    Option to include it (or not)
    Can select between two sizes (6” or 8”)
    Can set height and project length of the sump outlet
    Select flange options for the outlet, including flange type and end connection

## Slide 33: Overview and Demonstration
Let’s make a tank!