## Slide 1: Automation Starter Kit: Tank Body Details
Nathan Eliason
Senior Technical Consultant
Version 1.0 – June 2020

## Slide 2: Main Components
Shell Plates
Dish Head
Tank Body Assembly

## Slide 3: Shell Plates
Individual plates rolled and welded together to form the main tank body
Sheet Metal Component
Main Driving Parameters:
  TANK_OD (OD of tank)
  SHELL_THK (Shell thickness)
  SHELL_W (Shell width)
Component Rules:
  Shell Thickness (not currently in use)

## Slide 4: Shell Plates
Shell Thickness Rule:
  Sets the Sheet Metal style based on thickness

## Slide 5: Dish Head
Used to cap both ends of the tank body
Is an iPart with configurations for all dimensions in scope for the project
Main Driving Parameters:
  Size
  Thickness
Component Rules:
  None

## Slide 6: Tank Body Assembly
  MANWAY_VERT_OFF
  MANWAY
  GUNLINE
  F_HATCH
  F_HATCH_OFF
  R_HATCH
  R_HATCH_OFF
  INLET_OFF
Main assembly for tank body
Main Driving Parameters:
  PROJECT_ID
  PROJECT_PATH
  TANK_OD
  TANK_L
  SHELL_W_1
  SHELL_Q_1
  SHELL_W_2
  SHELL_Q_2
  GUNLINE_HOF_OFF
  GUNLINE_VERT_OFF
  GUNLINE_SIZE

## Slide 7: Tank Body Assembly
Component Rules:
  Calculate and Place Shells
    Creates new shell assy from template
    Places it in the correct folder
    Creates copies of shell plates
    Inserts shell plates into assembly
      Uses constraints to place components
      Staggers the seam for each shell
    Pushes parameters to each of the shells that were created
    Suppresses assembly cuts for features not needed in the specific tank configuration

## Slide 8: Inlets and Drains
Component Rules:
  Size Dish
    Changes the active instance of the iPart based on OD and thickness
    Note that for the current version, we only use the .25” thickness option in the dataset